## Slide 1: Turtlebot following a straight line by observing a square
Group 6 Project 6:
Rosh Dela Cruz – 14264764
Matthew Egan - 14289692
Daniel Lo - 14289716

## Slide 2: Project overview
To utilise ROS in Ubuntu 18.04.
To utilise a Turtlebot3 in the Gazebo environment.
GOAL: to manipulate a Turtlebot to follow a straight line by observing a feature rich square with an RGB-D camera.
Square image is placed within observable range, containing a grid layout for corners and an image of a car
To implement and use image processing algorithms.
To implement a PD controller to manipulate movement of Turtlebot to goal.

## Slide 3: Project timeline

## Slide 4: Methodology
To initialise the ROS environment
  Subscribing to topics/nodes, to receive data for Turtlebot
  Building Gazebo environment, designing square image and features
Image data extraction and processing
  Turtlebot will rotate on position to determine location of square image
  Utilise an initial image to feature of square image against
  SURF edge detection to identify the image and features are accurate
  Determine position relative to square
PD Controller
  Calculates error between orientation of Turtlebot to target and creates adjustments to movement and control.
    Turtlebot will first face parallel to target square and move in a straight line
    Moves forward until square is perpendicular to Turtlebot
    Once facing square, rotates 90 degrees until directly in front
  Sends ROS messages e.g. linear and angular velocity to move Turtlebot to position of Square image

## Slide 5: ROS graph

## Slide 6: Experiments
SURF detection
KAZE detection
MATLAB profiler
  Computational/memory usage
  Total run time
  Function usage
Gazebo simulation/world building
  Implementation of walls, surfaces
  Creation of Square image and development over time to test variety of patterns and features

## Slide 7: Project issues/difficulties
Simulation running was inconsistent across team members and computers
Gazebo environment crashing, lack of computational power
Orientation calculation issues
Development of square image and image processing working consistently

## Slide 8: Project video demo and results

## Slide 9: Final results

## Slide 10: Thanks for watching